## Slide 1: National Transonic Facility Public Geometry Release and Summary
Brent Pomeroy
Configuration Aerodynamics Branch
NASA Langley Research Center
Scott Brynildsen & Norma Farr
Geometry Lab Group
NASA Langley Research Center
Melissa Rivers
Transformational Tools and Technologies Project
NASA Langley Research Center
Ben Rider
High Speed Aerodynamics, Flight Sciences
Boeing Commercial Airplanes
Eric Walker
Chief Engineer for Test Operation Excellence and Research Directorate Chief Engineer Council Chair
NASA Langley Research Center
Seyedeh Sheida Hosseini
Transformational Tools and Technologies Project
NASA Ames Research Center

## Slide 2: Outline
Facility Overview
History
Key CRM Tests
CRM Coordinate Transformations
Geometry Files

## Slide 3: Facility Overview
Closed circuit, pressurized, cryogenic facility
Located at NASA Langley Research Center in Hampton, VA, USA
Facilitates transonic, flight Reynolds number (Re) testing
  Mach 0.1 to 1.2
  Re 4.0 million to 145 million/foot 1.2 million to 44 million/meter
  Temperature -250 to 130 deg F (-157 to 54 C; 116 to 328 K)
  Can operate with dry, ambient air or with gaseous nitrogen
Source: NASA

## Slide 4: Key Historical Dates
1960s Facility needs identification
1970-1973 Conceptual design
1971-1973 Risk reduction facility tests
1974-1978 Detailed design
1976 Funding appropriated
1979 Construction started
1982 Construction complete
1984 Open for production
2001 Aerospace Sciences Meeting (first open discussion of capabilities)

## Slide 5: History and Conceptual Design
Established an international need for high Reynolds number testing
  Desired for decades before construction
  Interest from academia, industry, and government
Detailed facility requirements study formalized in 1971
  Matured by Department of Defense, NASA, commercial partners, and scientific advisory committees
  Many workshops with partners and customers
Identified three ways to increase Reynolds number
  Increase Ptotal
  High molecular weight fluid
  Reduce Ttotal

## Slide 6: Configuration Selection
Two final configurations candidates
  Short-run, high-pressure Ludwieg tube
  Continuous-run cryogenic nitrogen facility
Cryo facility selected for five key reasons
  Temperature has a large effect on Reynolds number at low temperatures
  High Reynolds numbers can be tested
  Reduced temperature  reduced speed of sound  decreased velocity  decreased fan power
  Cryo nitrogen is similar to ambient, high-altitude flight conditions
  Independent control of total pressure, total temperature and fan speed

## Slide 7: Risk-Reduction Facilities
Two risk-reduction facilities constructed prior to NTF funding approval
Low-speed cryogenic benchtop wind tunnel (1971)
  7 inch by 11 inch (18 cm by 28 cm) test section
  Low speed (up to Mach 0.2)
  Operated down to 80 K (-316 F, -193 C)
  Confirmed liquid nitrogen injectors can create cryo conditions
  Identified requisite material behavior at cryo temperatures
Langley 0.3-Meter Transonic Cryogenic Tunnel (1973)
  Small-scale version of proposed NTF
  Transonic, cryogenic
  Designed to operate for 90 days; still in operation for technology-development experiments
Funding for NTF appropriated in 1976

## Slide 8: Test Environment Challenges
Materials advancements needed to ensure facility and model integrity
Japan Steel material improvements
  Developed high-strength 9% Nickel maraging steel
  Stronger materials and increased maximum part size than availably domestically
  Urban legend that Japan Steel was used due to a domestic steel shortage
Samurai sword friendship gift
  Made with traditional techniques
  Offered to NASA “... in hope that this sword would serve as a symbol of the international cooperation reflected in the National Transonic Facility”
  Sword is on display in the NTF building
Source: NASA

## Slide 9: Facility Digital Model
Detailed digital scan of NTF circuit was taken in the mid-2010s
  About 250 million points
  Approximately 80% of the points are in the plenum
  Significant work with GeoMagic used to generate CFD-ready surface geometry
High-speed leg geometry and model support hardware has been released
Point cloud data
Tunnel circuit, high speed leg (green), and plenum (blue)

## Slide 10: Key Common Research Model (CRM) Tests
CRM
  Original transonic tests performed in support of Drag Prediction Workshop IV
  High-quality experimental data facilitated detailed CFD comparisons
  Tests NTF-197, NTF-215, and NTF-229
CRM-HL
  Low-speed NTF test supplemented already-existing data sets
  Special session Wednesday morning in Academy 415 (GT-10/APA-26)
  Test NTF-237
CRM-NLF
  Designed with Crossflow-Attenuated Natural Laminar Flow (CATNLF) method
  Temperature-sensitive paint used to visualize regions of laminar/turbulent flow
  Test NTF-228

## Slide 11: Coordinate Transformation Overview
Different models require different transformations
  Full-span, upper-swept strut mounted vehicle
  Semispan, sidewall mounted vehicle
Four main steps
  Rig the full-scale vehicle in the tunnel at model scale
  Add sidewall standoff, if necessary
  Rotate mounting hardware to achieve zero-deg alpha, if necessary
  Rotate vehicle and associated hardware for non-zero alpha

## Slide 12: CRM Mounting Options
2.7% full-span
  Traditional CRM
  CRM-HL (planned test)
  Upper swept strut
5.2% semispan
  CRM-HL (GT-10/APA-26, Wednesday morning, Academy 415)
  CRM-NLF
2.7% semispan CRM-HL (planned test)
Coordinate transformations provided in the accompanying paper
Two example transformations on the next two slides

## Slide 13: Full-Span 2.7% CRM Coordinate Transformations
Source: NASA
how_mounted_2p7.txt
Equations maintained from previously-listed information for consistency
Transformations included in in CAD release
  Scale vehicle
  Translate to model origin in the wind tunnel
  Rotate arc sector and upper-swept strut around y axis
  Rotate arc sector, upper-swept strut, and vehicle for non-zero alpha
Animation depicting coordinate transformations

## Slide 14: Semispan 5.2% CRM Coordinate Transformations
how_mounted_5p2semispan.txt
Source: NASA
Version 1.9 has new transformations from historically published transformations
Transformations included in in the CAD release
  Translate and scale to wind tunnel model origin
  Add a standoff between the model and the wall
  Rotate vehicle for non-zero alpha
Animation depicting coordinate transformations

## Slide 15: Semispan 2.7% CRM Coordinate Transformations
how_mounted_2p7semispan.txt
Version 1.9 has transformations not previously published
Transformations included in in the CAD release
  Translate and scale to wind tunnel model origin
  Add a standoff between the model and the wall
  Rotate vehicle for non-zero alpha
Animation depicting coordinate transformations

## Slide 16: High-Speed Leg and Plenum

## Slide 17: Geometry Download
Posted to the new DPW website ( )
Note the new domain
Current version: v1.9 (June, 2025)
Contains
  12 files
  .igs, .stp, and .x_t
  All in inches
https://www.aiaa-dpw.org/ntf.html

## Slide 18: Geometry Overview

## Slide 19: Geometry Files (1/2)
Note: The diffuser extension is not part of the NTF. It is provided in the CAD so boundary conditions can be applied further away from the test section. This may be desired to avoid potential numerical problems at the end of the diffusor. Use is optional.

## Slide 20: Geometry Files (2/2)

## Slide 21: DPW-8/AePW-4 Usage
Test case for Test Environments Working Group
Consistent shift of CFD results relative to experimental data
Multiple items may cause the differences
  Wall effects?
  Tare and interference?
  Physical geometry differences?
  Freestream (i.e., inlet) conditions?
Complex geometry will require meticulous preparation and careful gridding

## Slide 22: Conclusions
NTF has a storied history of tests, including three CRM configurations
Detailed digitization of NTF circuit
Publicly available high-speed leg CAD has been released (v1.9) at https://www.aiaa-dpw.org/ntf.html
Test case of interest for DPW-8/AePW-4 Test Environment Working Group

## Slide 23: Special Thanks
Chris Rumsey
Miranda Ertsgaard
Courtney Winski
Andy Kwok